## Slide 1: Media Access Control Chapter 6
TexPoint fonts used in EMF.
Read the TexPoint manual before you delete this box.: AAAAAAAA

## Slide 2: Home Automation
Cooperative Lights, Blinds, Fans
Energy Monitoring
Security
  Intrusion Detection
  Fire Alarm
Digitalstrom
  EU: 10 billion electrical devices
  95% are not networked
  cheap networking (over power)
  true standby
  remote control
  universal ID
  …

## Slide 3: Rating
Area maturity
Practical importance
Theory appeal
First steps Text book
No apps Mission critical
Boooooooring Exciting

## Slide 4: Overview
Motivation
Classification
MAC layer techniques
Case study: 802.11

## Slide 5: Motivation
Can we apply media access methods from fixed networks?
Example CSMA/CD
  Carrier Sense Multiple Access with Collision Detection
  send as soon as the medium is free, listen into the medium if a collision occurs (original method in IEEE 802.3)
Problems in wireless networks
  signal strength decreases quickly with distance
  senders apply CS and CD, but the collisions happen at receivers
  Energy efficiency: having the radio turned on costs almost as much energy as transmitting, so to seriously save energy one needs to turn the radio off!

## Slide 6: Motivation – Hidden Terminal Problem
A sends to B, C cannot receive A
C wants to send to B, C senses a “free” medium (CS fails)
collision at B, A cannot receive the collision (CD fails)
A is “hidden” for C
B
A
C

## Slide 7: Motivation – Exposed Terminal Problem
B sends to A, C wants to send to D
C has to wait, CS signals a medium in use
since A is outside the radio range of C waiting is not necessary
C is “exposed” to B
B
A
C
D

## Slide 8: Motivation - Near and Far Terminals
Terminals A and B send, C receives
  the signal of terminal B hides A’s signal
  C cannot receive A
This is also a severe problem for CDMA networks
precise power control required
A
B
C

## Slide 9: Access Methods
SDMA (Space Division Multiple Access)
  segment space into sectors, use directed antennas
  Use cells to reuse frequencies
FDMA (Frequency Division Multiple Access)
  assign a certain frequency to a transmission channel
  permanent (radio broadcast), slow hopping (GSM), fast hopping (FHSS, Frequency Hopping Spread Spectrum)
TDMA (Time Division Multiple Access)
  assign a fixed sending frequency for a certain amount of time
CDMA (Code Division Multiple Access)
Combinations!
Notes: 15

## Slide 10: Multiplexing: Space Multiplexing
Multiplex channels (k) in four dimensions
  space (s)
  time (t)
  frequency (f)
  code (c)
Goal: multiple use of a shared medium
Important: guard spaces needed!
Example: radio broadcast
s2
s3
s1
f
t
c
k2
k3
k4
k5
k6
k1
f
t
c
f
t
c
channels ki

## Slide 11: Example: Cellular network
Simplified hexagonal model
Signal propagation ranges: Frequency reuse only with a certain distance between the base stations
Can you reuse frequencies in distance 2 or 3 (or more)?
Graph coloring problem
Interference from neighbor cells (other color) can be controlled with transmit and receive filters
Example: fixed frequency assignment for reuse with distance 2

## Slide 12: Signal-to-Noise
Digital techniques can withstand a signal to noise ratio (S/N) of approximately 9 dB, depending on the techniques…
Assume the path loss exponent  = 3. Then, which gives D/R = 3. Reuse distance of 2 might just work…
Remark: Signal-to-noise is also known as, e.g. carrier-to-interference ratio C/I.
D
R

## Slide 13: Frequency Division Multiplex (FDM)
Separation of the whole spectrum into smaller frequency bands
A channel gets a certain band of the spectrum for the whole time
+ no dynamic coordination necessary
+ works also for analog signals
– waste of bandwidth if traffic is distributed unevenly
– inflexible
Example: broadcast radio
k2
k3
k4
k5
k6
k1
f
t
c

## Slide 14: FDD/FDMA - general scheme, example GSM @ 900Mhz
f
t
124
1
124
1
20 MHz
200 kHz
890.2 MHz
935.2 MHz
915 MHz
960 MHz

## Slide 15: Time Division Multiplex (TDM)
f
t
c
k2
k3
k4
k5
k6
k1
A channel gets the whole spectrum for a certain amount of time
+ only one carrier in the medium at any time
+ throughput high even for many users
– precise synchronization necessary
Example: Ethernet

## Slide 16: TDD/TDMA - general scheme, example DECT
1
2
3
11
12
1
2
3
11
12
t
downlink
uplink
417 µs

## Slide 17: Time and Frequency Division Multiplex
f
Combination of both methods
A channel gets a certain frequency band for some time
+ protection against frequency selective interference
+ protection against tapping
+ adaptive
– precise coordination required
Example: GSM
t
c
k2
k3
k4
k5
k6
k1

## Slide 18: Code Division Multiplex (CDM)
Each channel has a unique code
All channels use the same spectrum at the same time
+ bandwidth efficient
+ no coordination or synchronization
+ hard to tap
+ almost impossible to jam
– lower user data rates
– more complex signal regeneration
Example: UMTS
Spread spectrum
U. S. Patent 2‘292‘387, Hedy K. Markey (a.k.a. Lamarr or Kiesler) and George Antheil (1942)
k2
k3
k4
k5
k6
k1
f
t
c

## Slide 19: Code Division Multiple Access (CDMA)
CDMA is a novel Physical/MAC concept.
Example: Direct Sequence Spread Spectrum (DSSS)
Each station is assigned an m-bit code (or chip sequence)
Typically m = 64, 128, ... (in our examples m = 4, 8, …)
To send 1 bit, station sends chip sequence
To send 0 bit, station sends complement of chip sequence
Instead of splitting a 1 MHz band shared between 100 channels into 100 x 10kHz bands, every station can use the whole band, with 100 chips.
  CDMA does not increase the total bandwidth, but it may simplify the MAC layer at the expense of complicating the physical layer.

## Slide 20: CDMA Basics

## Slide 21: CDMA Example
Assume that all stations are perfectly synchronous
Assume that all codes are pair wise orthogonal
Assume that if two or more stations transmit simultaneously, the bipolar signals add up linearly
Example
S = (+ – + – + – + –)
T = (+ + – – – + + –)
U = (+ – – + – – + +)
Check that codes are pair wise orthogonal
E.g., if S,T,U transmit simultaneously, a receiver receives R = S+T+U = (+3, –1, –1, –1, –1, –1, +3, –1)

## Slide 22: CDMA Example (2)
To decode a received signal R for sender s, one needs to calculate the normalized inner product R∙S.
R∙S = (+3, –1, –1, –1, –1, –1, +3, –1)∙(+ – + – + – + –)/8 = (+3+1–1+1–1+1+3+1)/8 = 8/8 = 1 … by accident?
R∙S = (S+T+U)∙S = S∙S +T∙S +U∙S = 1 + 0 + 0 = 1
With orthogonal codes we can safely decode the original signals

## Slide 23: CDMA: Construction of orthogonal codes with m chips
Note that we cannot have more than m orthogonal codes with m chips because each code can be represented by a vector in the m-dimensional space, and there are not more than m orthogonal vectors in the m-dimensional space.
Walsh-Hadamard codes can be constructed recursively (for m = 2k):
Code tree:
Note: Random codes are also quite balanced and pretty orthogonal.

## Slide 24: CDMA: How much noise can we tolerate?
We now add random noise:
R’ = R + N, where N is an m-digit noise vector.
Assume that chipping codes are balanced (as many “+” as “–”)
If N = (α, α, …, α) for any (positive or negative) α, then the noise N will not matter when we decode the received signal.
R’∙S = (R+N)∙S = S∙S +(orthogonal codes)∙S +N∙S = 1 + 0 + 0 = 1
How much random (white) noise can we tolerate?

## Slide 25: CDMA: Problems
Some of our assumptions are problematic:
It is not possible to synchronize chips perfectly. What can be done is that the sender first transmits a long enough known chip sequence on which the receiver can lock onto.
Not all stations are received with the same power level. CDMA is typically used for systems with fixed base stations. Then mobile stations can send with the reciprocal power they receive from the base station. (Alternatively: First decode the best station, and then subtract its signal to decode the second best station…)
We didn’t discuss how to transmit bits with electromagnetic waves.

## Slide 26: CDMA: Summary
+ all terminals can use the same frequency, no planning needed
+ reduces frequency selective fading and interference
+ base stations can use the same frequency range
+ several base stations can detect and recover the signal
+ soft handover between base stations
+ forward error correction and encryption can be easily integrated
– precise power control necessary
– higher complexity of receiver and sender
Example: UMTS

## Slide 27: Cocktail party as analogy for multiplexing
Space multiplex: Communicate in different rooms
Frequency multiplex: Use soprano, alto, tenor, or bass voices to define the communication channels
Time multiplex: Let other speaker finish
Code multiplex: Use different languages and hone in on your language. The “farther apart” the languages the better you can filter the “noise”: German/Japanese better than German/Dutch. Can we have orthogonal languages?

## Slide 28: Comparison SDMA/TDMA/FDMA/CDMA
[J.Schiller]

## Slide 29: MAC Alphabet Soup
μ-MAC
Aloha
AI-LMAC
B-MAC
BitMAC
BMA
CMAC
Crankshaft
CSMA-MPS
CSMA/ARC
DMAC
E2-MAC
EMACs
PicoRadio
PMAC
PMAC‘
Preamble sampling
Q-MAC
Q-MAC’
QMAC
RATE EST
RL-MAC
RMAC
RMAC’
S-MAC
S-MAC/AL
f-MAC
FLAMA
Funneling-MAC
G-MAC
HMAC
LMAC
LPL
MMAC
nanoMAC
O-MAC
PACT
PCM
PEDAMACS
SMACS
SCP-MAC
SEESAW Sift
SS-TDMA
STEM
T-MAC
TA-MAC
TRAMA
U-MAC
WiseMAC
X-MAC
Z-MAC
[TU Delft]

## Slide 30: Traditional MAC Protocol Classification
Centralized/Single-Hop Protocols
  A base station coordinates all traffic
Contention Protocols (CSMA)
  Transmit when you feel like transmitting
  Retry if collision, try to minimize collisions, additional reservation modes
  Problem: Receiver must be awake as well
Scheduling Protocols (TDMA)
  Use a “pre-computed” schedule to transmit messages
  Distributed, adaptive solutions are difficult
Hybrid protocols
  E.g. contention with reservation  scheduling
  Specific (“cross-layer”) solutions, e.g. Dozer for data gathering

## Slide 31: Polling mechanisms
If one terminal can be heard by all others, this “central” terminal (a.k.a. base station) can poll all other terminals according to a certain scheme
  Use a scheme known from fixed networks
  The base station chooses one address for polling from the list of all stations
  The base station acknowledges correct packets and continues polling the next terminal
  The cycle starts again after polling all terminals of the list

## Slide 32: Example: Inhibit Sense Multiple Access (ISMA)
Current state of the medium is signaled via a “busy tone”
the base station signals on the downlink (base station to terminals) whether the medium is free
terminals must not send if the medium is busy
terminals can access the medium as soon as the busy tone stops
the base station signals collisions and successful transmissions via the busy tone and acknowledgements, respectively (media access is not coordinated within this approach)
Example: for CDPD (USA, integrated into AMPS)

## Slide 33: TDMA – Motivation
System with n stations (0,1,2,…,n–1) and one shared channel
The channel is a perfect broadcast channel
  Single transmissions are received by every other station.
  No hidden or exposed terminal problem.
  Interference if more than one station transmits.
Round robin algorithm: station k sends after station k–1 (mod n)
  If a station does not need to transmit data, then it sends “ε”
  There is a maximum message size m that can be transmitted
How efficient is round robin? What if a station breaks or leaves?
All deterministic TDMA protocols have these (or worse) problems

## Slide 34: TDMA – Slotted Aloha
We assume that the stations are perfectly synchronous
In each time slot each station transmits with probability p.
In Slotted Aloha, a station can transmit successfully with probability at least 1/e, or about 36% of the time.

## Slide 35: Backoff Protocols
Backoff protocols rely on acknowledgements only.
Binary exponential backoff
  If a packet has collided k times, we set p = 2-k
  Or alternatively: wait from random number of slots in [1..2k]
It has been shown that binary exponential backoff is not stable for any arrival rate λ > 0 (if there are infinitely many potential stations)
  [Proof sketch: with very small but positive probability you go to a bad situation with many waiting stations, and from there you get even worse with a potential function argument – sadly the proof is too intricate to be shown in this course ]
Interestingly when there are only finite stations, binary exponential backoff becomes unstable with λ > 0.568; Polynomial backoff however, remains stable for any λ < 1.

## Slide 36: Demand Assigned Multiple Access (DAMA)
Channel efficiency is only 36% for Slotted Aloha, and even worse for backoff protocols.
Practical systems therefore use reservation whenever possible.
  But: Every scalable system needs an Aloha style component.
Reservation:
  a sender reserves a future time-slot
  sending within this reserved time-slot is possible without collision
  reservation also causes higher delays
Examples for reservation algorithms on the following slides
  typical scheme for satellite systems

## Slide 37: DAMA: Explicit Reservation
Aloha mode for reservation: competition for small reservation slots, collisions possible.
Reserved mode for data transmission within successful reserved slots (no collisions possible).
It is important for all stations to keep the reservation list consistent at any point in time and, therefore, all stations have to synchronize from time to time.
Aloha
reserved
Aloha
reserved
Aloha
reserved
Aloha
collisions
t
reserved
Notes: 24

## Slide 38: DAMA: Implicit Reservation
A certain number of slots form a frame, frames are repeated.
Stations compete for empty slots according to the slotted aloha principle.
Once a station reserves a slot successfully, this slot is automatically assigned to this station in all following frames.
Competition for this slots starts again as soon as the slot was empty in the last frame .
frame1
frame2
frame3
frame4
frame5
1
2
3
4
5
6
7
8
time-slot
collision at reservation attempts
A
C
D
A
B
A
F
A
C
A
B
A
A
B
A
F
A
B
A
F
D
A
C
E
E
B
A
F
D
t
ACDABA-F
ACDABA-F
AC-ABAF-
A---BAFD
ACEEBAFD
reservation
Notes: 25

## Slide 39: DAMA: Reservation TDMA
Every frame consists of n mini-slots and x data-slots
Every station has its own mini-slot and can reserve up to k data-slots using this mini-slot (i.e. x = nk).
Other stations can send data in unused data-slots according to a round-robin sending scheme (best-effort traffic)
N mini-slots
Nk data-slots
reservations for data-slots
other stations can use free data-slots
based on a round-robin scheme
n=6, k=2
Notes: 26

## Slide 40: Multiple Access with Collision Avoidance (MACA)
Use short signaling packets for collision avoidance
  Request (or ready) to send RTS: a sender requests the right to send from a receiver with a short RTS packet before it sends a data packet
  Clear to send CTS: the receiver grants the right to send as soon as it is ready to receive
Signaling packets contain
  sender address
  receiver address
  packet size
Example: Wireless LAN (802.11) as DFWMAC

## Slide 41: MACA examples
MACA avoids the problem of hidden terminals
  A and C want to send to B
  A sends RTS first
  C waits after receiving CTS from B
MACA avoids the problem of exposed terminals
  B wants to send to A, and C to D
  now C does not have to wait as C cannot receive CTS from A
A
B
C
RTS
CTS
CTS
A
B
C
RTS
CTS
RTS
D

## Slide 42: Energy Efficient MAC Protocols
In sensor networks energy is often more critical than throughput.
  The radio component should be turned off as much as possible.
Energy management considerations have a big impact on MAC protocols.
  Idle listening costs about as much energy as transmitting
In the following we present a few ideas, stolen from some known protocols that try to balance throughput and energy consumption.
  S-MAC, T-MAC, B-MAC, or WiseMAC
Many of the hundreds of MAC protocols that were proposed have similar ideas…

## Slide 43: Sensor MAC (S-MAC)
Coarse-grained TDMA-like sleep/awake cycles.
All nodes choose and announce awake schedules.
  synchronize to awake schedules of neighboring nodes.
Uses RTS/CTS to resolve contention during listen intervals.
  And allows interfering nodes to go to sleep during data exchange.
listen
sleep
sleep
listen
frame
time
increased latency

## Slide 44: Sensor MAC (S-MAC)
Problem: Nodes may have to follow multiple schedules to avoid network partition.
Schedule 1
Schedule 2
Schedule 1+2
A fixed sleep/awake ratio is not always optimal.
  Variable load in the network.
Idea: Adapt listen interval dependent on the current network load.
  T-MAC

## Slide 45: Low Power Listening (B-MAC)
Nodes wake up for a short period and check for channel activity.
  Return to sleep if no activity detected.
If a sender wants to transmit a message, it sends a long preamble to make sure that the receiver is listening for the packet.
  preamble has the size of a sleep interval
Very robust
  No synchronization required
  Instant recovery after channel disruption
preamble
data
listen
channel sniff

## Slide 46: Low Power Listening (B-MAC)
Problem: All nodes in the vicinity of a sender wake-up and wait for the packet.
  Solution 1: Send wake-up packets instead of preamble, wake-up packets tell when data is starting so that receiver can go back to sleep as soon as it received one wake-up packet.
  Solution 2: Just send data several times such that receiver can tune in at any time and get tail of data first, then head.
Communication costs are mostly paid by the sender.
  The preamble length can be much longer than the actual data length.
Idea: Learn wake-up schedules from neighboring nodes.
  Start sending preamble just before intended receiver wakes up.
  WiseMAC
  overhearing problem
  encode wake-up pattern in ACK message

## Slide 47: Hybrid Protocols
Protocols may use information from upper layers to further improve their performance.
  Information about neighborhood
  Routing policies
Minimize costly overhearing of neighboring nodes
  Inform them to change their channel sniff patterns
Use randomization to resolve schedule collisions
schedule collision
optimization for WiseMAC
like in Dozer

## Slide 48: Standards
IEEE 802.15.4
  physical & MAC layer
  star, clique (peer-to-peer), and cluster tree topology
  Full function (with coordinator) and reduced function nodes
  Unslotted mode (nonbeacon)
    CSMA/CA: Send when medium is free
  Slotted mode (beacon)
    Similar to beacons in Dozer: Coordinator sends beacon to indicate period when nodes can send
Protocols on higher layers using 802.15.4
  ZigBee
    Goals: low cost, low power (not really), plug-in and short range
  TSMP (Time Synchronized Mesh Protocol)
    Goals: reliability and low power

## Slide 49: Case Study: 802.11 – Design Goals
Global, seamless operation
Low power consumption for battery use
No special permissions or licenses required
Robust transmission technology
Simplified spontaneous cooperation at meetings
Easy to use for everyone, simple management
Interoperable with wired networks
Security (no one should be able to read my data), privacy (no one should be able to collect user profiles), safety (low radiation)
Transparency concerning applications and higher layer protocols, but also location awareness if necessary

## Slide 50: 802.11 Characteristics
+ Very flexible (economical to scale)
+ Ad-hoc networks without planning possible
+ (Almost) no wiring difficulties (e.g. historic buildings, firewalls)
+ More robust against disasters or users pulling a plug
– Low bandwidth compared to wired networks (20 vs. 1000 Mbit/s)
– Many proprietary solutions, especially for higher bit-rates, standards take their time
– Products have to follow many national restrictions if working wireless, it takes a long time to establish global solutions (IMT-2000)
– Security
– Economy

## Slide 51: 802.11 Infrastructure vs. ad hoc mode
Infrastructure
network
Ad-hoc network
AP
AP
AP
wired network
AP: Access Point

## Slide 52: 802.11 – Protocol architecture
mobile terminal
access point
server
fixed terminal
application
TCP
802.11 PHY
802.11 MAC
IP
802.3 MAC
802.3 PHY
application
TCP
802.3 PHY
802.3 MAC
IP
802.11 MAC
802.11 PHY
LLC
infrastructure network
LLC
LLC

## Slide 53: 802.11 – The lower layers in detail
PMD (Physical Medium Dependent)
  modulation, coding
PLCP (Physical Layer Convergence Protocol)
  clear channel assessment signal (carrier sense)
PHY Management
  channel selection, PHY-MIB
Station Management
  coordination of all management functions
MAC
  access mechanisms
  fragmentation
  encryption
MAC Management
  Synchronization
  roaming
  power management
  MIB (management information base)
PMD
PLCP
MAC
LLC
MAC Management
PHY Management
PHY
DLC
Station Management

## Slide 54: MAC layer: DFWMAC
Traffic services
  Asynchronous Data Service (mandatory)
    exchange of data packets based on “best-effort”
    support of broadcast and multicast
  Time-Bounded Service (optional)
    implemented using PCF (Point Coordination Function)
Access methods
  DFWMAC-DCF CSMA/CA (mandatory)
    collision avoidance via binary exponential back-off mechanism
    minimum distance between consecutive packets
    ACK packet for acknowledgements (not used for broadcasts)
  DFWMAC-DCF w/ RTS/CTS (optional)
    avoids hidden terminal problem
  DFWMAC-PCF (optional)
    access point polls terminals according to a list

## Slide 55: MAC layer
defined through different inter frame spaces
no guaranteed, hard priorities
SIFS (Short Inter Frame Spacing)
  highest priority, for ACK, CTS, polling response
PIFS (PCF IFS)
  medium priority, for time-bounded service using PCF
DIFS (DCF, Distributed Coordination Function IFS)
  lowest priority, for asynchronous data service
t
medium busy
SIFS
PIFS
DIFS
DIFS
next frame
contention
direct access if medium is free  DIFS

## Slide 56: CSMA/CA
station ready to send starts sensing the medium (Carrier Sense based on CCA, Clear Channel Assessment)
if the medium is free for the duration of an Inter-Frame Space (IFS), the station can start sending (IFS depends on service type)
if the medium is busy, the station has to wait for a free IFS, then the station must additionally wait a random back-off time (collision avoidance, multiple of slot-time)
if another station occupies the medium during the back-off time of the station, the back-off timer stops (fairness)
t
medium busy
DIFS
DIFS
next frame
contention window
(randomized back-off mechanism)
slot time
direct access if medium is free  DIFS
Notes: 12

## Slide 57: Competing stations - simple example
t
busy
boe
station1
station2
station3
station4
station5
packet arrival at MAC
DIFS
boe
boe
boe
busy
elapsed backoff time
bor
residual backoff time
busy
medium not idle (frame, ack etc.)
bor
bor
DIFS
boe
boe
boe
bor
DIFS
busy
busy
DIFS
boe
busy
boe
boe
bor
bor
backoff

## Slide 58: CSMA/CA 2
Sending unicast packets
  station has to wait for DIFS before sending data
  receivers acknowledge at once (after waiting for SIFS) if the packet was received correctly (CRC)
  automatic retransmission of data packets in case of transmission errors
t
SIFS
DIFS
data
ACK
waiting time
other
stations
receiver
sender
data
DIFS
contention

## Slide 59: DFWMAC
station can send RTS with reservation parameter after waiting for DIFS (reservation determines amount of time the data packet needs the medium)
acknowledgement via CTS after SIFS by receiver (if ready to receive)
sender can now send data at once, acknowledgement via ACK
other stations store medium reservations distributed via RTS and CTS
t
SIFS
DIFS
data
ACK
defer access
other
stations
receiver
sender
data
DIFS
contention
RTS
CTS
SIFS
SIFS
NAV (RTS)
NAV (CTS)

## Slide 60: Fragmentation
If packet gets too long transmission error probability grows
A simple back of the envelope calculation determines the optimal fragment size
t
SIFS
DIFS
data
ACK1
other
stations
receiver
sender
frag1
DIFS
contention
RTS
CTS
SIFS
SIFS
NAV (RTS)
NAV (CTS)
NAV (frag1)
NAV (ACK1)
SIFS
ACK2
frag2
SIFS

## Slide 61: Fragmentation: What fragment size is optimal?
Total data size: D bits
Overhead per packet (header): h bits
Overhead between two packets (acknowledgement): a “bits”
We want f fragments, then each fragment has k = D/f + h data + header bits
Channel has bit error probability q = 1-p
Probability to transmit a packet of k bits correctly: P := pk
Expected number of transmissions until packet is success: 1/P
Expected total cost for all D bits: f¢(k/P+a)
Goal: Find a k > h that minimizes the expected cost

## Slide 62: Fragmentation: What fragment size is optimal?
For the sake of a simplified analysis we assume a = O(h)
If we further assume that a header can be transmitted with constant probability c, that is, ph = c.
We choose k = 2h; Then clearly D = f¢h, and therefore expected cost
If already a header cannot be transmitted with high enough probability, then you might keep the message very small, for example k = h + 1/q

## Slide 63: DFWMAC-PCF
An access point can poll stations
PIFS
stations‘
NAV
wireless
stations
point
coordinator
D1
U1
SIFS
NAV
SIFS
D2
U2
SIFS
SIFS
SuperFrame
t0
medium busy
t1

## Slide 64: DFWMAC-PCF 2
t
stations‘
NAV
wireless
stations
point
coordinator
D3
NAV
PIFS
D4
U4
SIFS
SIFS
CFend
contention
period
contention free period
t2
t3
t4

## Slide 65: Frame format
Type
  control frame, management frame, data frame
Sequence control
  important against duplicated frames due to lost ACKs
Addresses
  receiver, transmitter (physical), BSS identifier, sender (logical)
Miscellaneous
  sending time, checksum, frame control, data
Frame
Control
Duration
ID
Address
1
Address
2
Address
3
Sequence
Control
Address
4
Data
CRC
2
2
6
6
6
6
2
4
0-2312
bytes
Byte 1: version, type, subtype
Byte 2: two DS-bits, fragm., retry, power man., more data, WEP, order

## Slide 66: MAC address format
DS: Distribution System
AP: Access Point
DA: Destination Address
SA: Source Address
BSSID: Basic Service Set Identifier
RA: Receiver Address
TA: Transmitter Address

## Slide 67: Special Frames: ACK, RTS, CTS
Acknowledgement
Request To Send
Clear To Send
Frame
Control
Duration
Receiver
Address
Transmitter
Address
CRC
2
2
6
6
4
bytes
Frame
Control
Duration
Receiver
Address
CRC
2
2
6
4
bytes
Frame
Control
Duration
Receiver
Address
CRC
2
2
6
4
bytes
ACK
RTS
CTS

## Slide 68: MAC management
Synchronization
  try to find a LAN, try to stay within a LAN
  timer etc.
Power management
  sleep-mode without missing a message
  periodic sleep, frame buffering, traffic measurements
Association/Reassociation
  integration into a LAN
  roaming, i.e. change networks by changing access points
  scanning, i.e. active search for a network
MIB - Management Information Base
  managing, read, write

## Slide 69: Synchronization
In an infrastructure network, the access point can send a beacon
beacon interval
t
medium
access
point
busy
B
busy
busy
busy
B
B
B
value of timestamp
B
beacon frame

## Slide 70: Synchronization
In an ad-hoc network, the beacon has to be sent by any station
t
medium
station1
busy
B1
beacon interval
busy
busy
busy
B1
value of the timestamp
B
beacon frame
station2
B2
B2
backoff delay

## Slide 71: Power management
Idea: if not needed turn off the transceiver
States of a station: sleep and awake
Timing Synchronization Function (TSF)
  stations wake up at the same time
Infrastructure
  Traffic Indication Map (TIM)
    list of unicast receivers transmitted by AP
  Delivery Traffic Indication Map (DTIM)
    list of broadcast/multicast receivers transmitted by AP
Ad-hoc
  Ad-hoc Traffic Indication Map (ATIM)
    announcement of receivers by stations buffering frames
    more complicated - no central AP
    collision of ATIMs possible (scalability?)

## Slide 72: Power saving with wake-up patterns (infrastructure)
TIM interval
t
medium
access
point
busy
D
busy
busy
busy
T
T
D
T
TIM
D
DTIM
DTIM interval
B
B
B
broadcast/multicast
station
awake
p
PS poll
p
d
d
d
data transmission
to/from the station

## Slide 73: Power saving with wake-up patterns (ad-hoc)
awake
A
transmit ATIM
D
transmit data
t
station1
B1
B1
B
beacon frame
station2
B2
B2
random delay
A
a
D
d
ATIM
window
beacon interval
a
acknowledge ATIM
d
acknowledge data

## Slide 74: WLAN: IEEE 802.11b
Data rate
  1, 2, 5.5, 11 Mbit/s, depending on SNR
  User data rate max. approx. 6 Mbit/s
Transmission range
  300m outdoor, 30m indoor
  Max. data rate <10m indoor
Frequency
  Free 2.4 GHz ISM-band
Security
  Limited, WEP insecure, SSID
Cost
  Low
Availability
  Declining

## Slide 75: WLAN: IEEE 802.11b
Connection set-up time
  Connectionless/always on
Quality of Service
  Typically best effort, no guarantees
  unless polling is used, limited support in products
Manageability
  Limited (no automated key distribution, sym. encryption)
+ Advantages: many installed systems, lot of experience, available worldwide, free ISM-band, many vendors, integrated in laptops, simple system
– Disadvantages: heavy interference on ISM-band, no service guarantees, slow relative speed only

## Slide 76: IEEE 802.11b – PHY frame formats
synchronization
SFD
signal
service
HEC
payload
PLCP preamble
PLCP header
128
16
8
8
16
variable
bits
length
16
192 µs at 1 Mbit/s DBPSK
1, 2, 5.5 or 11 Mbit/s
short synch.
SFD
signal
service
HEC
payload
PLCP preamble
(1 Mbit/s, DBPSK)
PLCP header
(2 Mbit/s, DQPSK)
56
16
8
8
16
variable
bits
length
16
96 µs
2, 5.5 or 11 Mbit/s
Long PLCP PPDU format
Short PLCP PPDU format (optional)

## Slide 77: Channel selection (non-overlapping)
2400
[MHz]
2412
2483.5
2442
2472
channel 1
channel 7
channel 13
Europe (ETSI)
US (FCC)/Canada (IC)
2400
[MHz]
2412
2483.5
2437
2462
channel 1
channel 6
channel 11
22 MHz
22 MHz

## Slide 78: WLAN: IEEE 802.11a
Data rate
  6, 9, 12, 18, 24, 36, 48, 54 Mbit/s, depending on SNR
  User throughput (1500 byte packets): 5.3 (6), 18 (24), 24 (36), 32 (54)
  6, 12, 24 Mbit/s mandatory
Transmission range
  100m outdoor, 10m indoor: e.g., 54 Mbit/s up to 5 m, 48 up to 12 m, 36 up to 25 m, 24 up to 30m, 18 up to 40 m, 12 up to 60 m
Frequency
  Free 5.15-5.25, 5.25-5.35, 5.725-5.825 GHz ISM-band
Security
  Limited, WEP insecure, SSID
Cost
  $50 adapter, $100 base station, dropping
Availability
  Some products, some vendors
  Not really deployed in Europe (regulations!)

## Slide 79: WLAN: IEEE 802.11a
Connection set-up time
  Connectionless/always on
Quality of Service
  Typically best effort, no guarantees (same as all 802.11 products)
Manageability
  Limited (no automated key distribution, sym. Encryption)
+ Advantages: fits into 802.x standards, free ISM-band, available, simple system, uses less crowded 5 GHz band
– Disadvantages: stronger shading due to higher frequency, no QoS

## Slide 80: Quiz: Which 802.11 standard?

## Slide 81: Open Problem
Although the MAC alphabet soup is constantly growing, the tradeoffs delay, throughput, energy-efficiency, locality, dynamics, fairness, … are still not understood. In particular there is no Swiss Army Knife of MAC protocols, with good guarantees in delay and throughput, even in dynamic situations.